## Slide 1
MSc PROJECT · ROS 2 JAZZY · TWO KINOVA GEN3 7-DOF
Multimodal Teleoperation of a Wearable Dual-Arm Supernumerary Robotic System
Master interface design, safety architecture, and a workspace characterisation
Gaus Sayyad
The arms are worn by one person and driven by a different person. Both are participants.
Every figure in this deck is regenerated from a committed recording by scripts/make_presentation.py

## Slide 2
CONTENTS
What this deck covers
Wearable dual-arm supernumerary robot · shared autonomy
1
1 · The problem
A third and fourth arm worn by someone who is not driving them
2 · The system as built
Master arm, five operating modes, and the safety architecture
3 · Perception and autonomy
Measure the environment, then plan against the measurement
4 · Results
Grasping, motion generation, VR, and the simulation-to-hardware gap
5 · Workspace characterisation
Why the arms barely move, sized rather than asserted
6 · Method, limits and next steps
What is verified, what is demonstration, and what is blocked
The deck is ordered as the thesis is: what was built, what was measured, and what the measurement does not support.
source: thesis_v2/main.tex — chapters 1-14

## Slide 3
PART 1
The problem
A supernumerary limb is not a prosthesis and not an industrial arm. Two people share one body's worth of space, and only one of them is in control.
2

## Slide 4
FRAMING
Two people, one body, one set of arms
Wearable dual-arm supernumerary robot · shared autonomy
3
The driver is across the room. The wearer carries 17 kg on a backpack frame and does not control the arms. A third person holds the emergency stop and watches the wearer, not the screen. This split is what makes the safety case different from ordinary teleoperation.
source: thesis_v2/figures/tikz/overview.tex

## Slide 5
OBJECTIVES
What the project set out to build
Wearable dual-arm supernumerary robot · shared autonomy
4
A master interface a person can actually drive
An instrumented mannequin arm over a Teensy 4.1, plus a VR route and a typed or spoken sentence — four ways into the same arms.
A safety case that survives the arms being worn
The wearer is in the collision model, the clearance floor is measured geometrically, and every refusal names what blocked it.
A workspace characterisation, sized rather than asserted
What limits the reach, by how much, and what each design choice costs in millimetres.
Autonomy that can be checked
From a typed sentence to four cubes placed by colour, with the camera's detections shown before anything moves.
An instrument discipline
Every analysis script carries a known-answer test, because the measuring tool has been the fault seventeen times.
The five objectives, and the order the rest of this deck follows.
source: docs/WORK_BRIEF.md, docs/TASK_SPEC.md

## Slide 6
PART 2
The system as built
Hardware, the master arm, the software architecture, the five operating modes, and the safety chain that gates all of them.
5

## Slide 7
AS BUILT
The hardware
Wearable dual-arm supernumerary robot · shared autonomy
6
Two Kinova Gen3, 7-DOF, Robotiq 2F-85
Mounted behind the wearer's shoulders on a backpack frame, 150 mm outboard and 15° of yaw from the shoulder line.
Master: an instrumented mannequin arm
14 channels over a Teensy 4.1 — roll and bend alternating along the chain.
ROS 2 Jazzy, 16 packages
Teleoperation imports nothing in-repo, so it stays the baseline condition of every comparison.
Host is WSL2
Which forces the high-level Kortex API: every cyclic write is a network round trip.
The arm shown is the vendor's product image. NO PHOTOGRAPH OF THE ASSEMBLED LAB RIG IS COMMITTED TO THIS REPOSITORY — every visual in this deck is a render, a screenshot or a diagram, and is labelled as such.
source: src/ros2_kortex/doc/resources/ — vendor image, not a lab photograph

## Slide 8
MASTER INTERFACE
The master arm, from CAD to kinematic chain
Wearable dual-arm supernumerary robot · shared autonomy
7
CAD, zero configuration
Chain: CAD against measured, mm
Roll and bend alternate along the chain. Link lengths are CAD-inferred and then checked against the measured arm — the two disagree by a few millimetres per link, and the measured value is the one the software uses.
source: thesis_v2/figures/master_arm_cad_views.png, master_arm_chain.png

## Slide 9
MASTER INTERFACE
Electronics and pin assignment
Wearable dual-arm supernumerary robot · shared autonomy
8
Fourteen channels over one Teensy 4.1. The call-out records why two analog-capable pins could not be used — a wiring constraint that later shows up in the channel health results.
source: thesis_v2/figures/diagrams/electronics.tex

## Slide 10
MEASURED
Master channel health — the honest picture
Wearable dual-arm supernumerary robot · shared autonomy
9
Seven of fourteen channels are incoherent — a soldering problem, with l_j2 and l_j4 named by regression. The system degrades rather than stopping: which channels are FROZEN is decided from the newest baseline, and a stale baseline freezes channels that now work.
source: recordings/baselines/channels_20260806.json (2026-08-06)

## Slide 11
ARCHITECTURE
Software architecture
Wearable dual-arm supernumerary robot · shared autonomy
10
Six srl_* packages. The dependency arrow runs one way: srl_teleop imports nothing in-repo, so the baseline condition of every experiment cannot be contaminated by the autonomy layer it is compared against.
source: thesis_v2/figures/diagrams/architecture.tex

## Slide 12
ARCHITECTURE
The data path, end to end
Wearable dual-arm supernumerary robot · shared autonomy
11
From a sensed master joint to a commanded arm joint, with every rate and every gate on the way.
source: thesis_v2/figures/tikz/datapath.tex

## Slide 13
OPERATING MODES
Driving the arms by hand: the mannequin, and VR
Wearable dual-arm supernumerary robot · shared autonomy
12
MODE 01 — instrumented mannequin arm over a Teensy 4.1
MODE 02 — two hand controllers as 6-DOF motion capture
Blue is sensing, grey is processing, red can stop the arm, green commands motion — the same colour law in every mode diagram.
source: thesis_v2/figures/diagrams/mode1_mannequin.tex, mode2_vr.tex

## Slide 14
OPERATING MODES
Sharing control, and giving up control entirely
Wearable dual-arm supernumerary robot · shared autonomy
13
MODES 03 / 04 — shared autonomy over either input path
MODE 06 — full autonomy from a typed or spoken sentence
The task layer commands the SAME waypoints under every mode — run_abc builds them with no mode argument — so any difference in what the robot does is a property of the mode, not of the task.
source: thesis_v2/figures/diagrams/mode3_shared.tex, mode4_voice.tex

## Slide 15
SAFETY
The safety chain
Wearable dual-arm supernumerary robot · shared autonomy
14
Three stages before any command leaves. Stage 3 measures the distance to the wearer from the shapes directly — it does not use the simulator's collision settings, because the SRDF deliberately excludes the 44 proximal pairs a shoulder mount actually threatens, and would report a clear pose with the tube inside the person.
source: thesis_v2/figures/tikz/safety.tex

## Slide 16
SAFETY
The wearer is in the collision model
Wearable dual-arm supernumerary robot · shared autonomy
15
RViz, home pose, both arms parked. The wearer's torso, head, hips and arms are all in the model, and the wearer's posture is a variable with one source — a posture that reaches the planner but not the clearance guard measures the old body under a new name.
source: thesis_v2/figures/rviz/home_pose_labelled.png; docs/img/presentation_pose_iso.png (2026-08-15)

## Slide 17
SAFETY · MEASURED
Clearance to the wearer, per task
Wearable dual-arm supernumerary robot · shared autonomy
16
The floor is 150 mm
and the mount alone sits 161 mm from the torso — so there are 11 mm of headroom before the arm does anything at all.
Only T1 stage 1 is clean
T0 breaches by ~142/137 mm, T2 by 150/147, T3's left arm by 88.
Predictive avoidance is worth 0.0–5.6 mm
All 28 refusals name end_effector_link: the hand is inside the person, and the null space holds the hand fixed by definition.
A breach is reported, not silenced. An SRDF exclusion silences an alarm; it does not move the metal.
source: recordings/baselines/home_change_applied.json, predictive_avoidance.json

## Slide 18
PART 3
Perception and autonomy
Measure the environment, then plan against the measurement — rather than against a scene someone typed in.
17

## Slide 19
PERCEPTION
The perception pipeline
Wearable dual-arm supernumerary robot · shared autonomy
18
Four cameras — both wrist RGB-D, a RealSense and a USB scene camera — reduced to a plane and a set of objects per camera per cycle, with per-camera health and named refusals.
source: thesis_v2/figures/tikz/perception.tex

## Slide 20
SAFETY CASE
The camera may only make the wearer BIGGER
Wearable dual-arm supernumerary robot · shared autonomy
19
fuse() keeps whichever body is CLOSER to the robot, per part, with no mode switch.
A tracked torso can sit beside a mannequin upper arm in one scene. A body injected 0.10 / 0.30 / 1.00 / 5.00 m FURTHER away changes nothing at all — which is the property that makes the camera safe to add.
fault injected through the live node
what must happen
result
the frame is dark
refuse, naming darkness
PASS
the frame is blank
refuse, naming a blank frame
PASS
two people in frame
refuse, naming the second person
PASS
nobody in frame
refuse, naming the empty frame
PASS
the arms are occluded
fall back per part, naming the occlusion
PASS
the body is pushed further away
ignore it — keep the mannequin
PASS
control: one person, clear frame
track, and say it is tracking
PASS
7 of 7 — and the requirement that a refusal NAME its own fault caught a false pass where the two-person gate had never run. The injected frames are stock test images, not lab photographs.
source: scripts/verify_wearer_fallbacks.py, src/srl_perception/test/test_wearer_tracking.py

## Slide 21
ENVIRONMENT MAPPING
The robot maps the workspace, then plans against the map
Wearable dual-arm supernumerary robot · shared autonomy
20
6 / 6
objects recovered
every one exact in x,y to a millimetre; every dimension within 3 mm
+0.2 mm
surface height error
against the renderer's own geometry
Objects are cut from the picture
segment_lift, not clustered from the point pile.
One wrist attitude per pass, pure translation
printer-probe style: 2 layers × 3 yaws × 2 arms.
74 of 74 reachable cells, 0 stillness refusals
and the sweep records what it can reach, then replans from it.
The earlier '−5.2 mm' surface error was surface_z reporting the plane's intercept AT THE ORIGIN, which is inside the wearer — an instrument fault, not a measurement.
source: recordings/session/20260824_190937/ ; docs/system/25_calibrate_then_plan.md

## Slide 22
ENVIRONMENT MAPPING
From the map to a pick
Wearable dual-arm supernumerary robot · shared autonomy
21
Table found at z = 1.2485 m, tilt 0.54°
bounds found by a coarse probe before the sweep, not typed in.
6 objects; 4 graspable at 41 mm, 2 refused at 140 mm
'too wide' is a named refusal — the gripper opens 85 mm.
Approached from ABOVE
pregrasp z 1.490 → grasp z 1.381 onto an object at z 1.282.
765 s end to end, 55 narration sentences
full scan, reference, pick and quick check, all exit 0.
DEMONSTRATION, not evidence: the arm is simulated and the depth is rendered. What is real is the sweep order, the deprojection, the segmentation, the fusion, the plane fit, the IK, the approach-angle search and every refusal.
source: recordings/session/20260824_190937/summary.txt (2026-08-24)

## Slide 23
MODE 06
Full autonomy: four cubes placed by colour, from a typed sentence
Wearable dual-arm supernumerary robot · shared autonomy
22
4 grasps, 4 releases
every cube on the pad of its own colour, started at home 0.0000 rad.
Both arms, pads at ±0.290 m
straddling the centreline — and neither arm can cross it, so a cube is only ever delivered to the pad on its own side.
Each clip runs card → look → task
the observe move is in the footage, and the card carries the sentence verbatim.
Four synchronised RViz views of one run. The wearer, the table, the two coloured pads and the four cubes are all in the scene the planner is checked against.
source: recordings/verification/06_full_autonomy/T1/S1_both_arms_centre/rviz_quad.mp4 (2026-08-23)

## Slide 24
MODE 06
A seeded layout, and the view where a grasp is judged
Wearable dual-arm supernumerary robot · shared autonomy
23
T1 stage 2 — seeded layout
T1 — the pads on the cube
Stage 2 is stage 1's geometry with the side drawn at random — eight seeds walked, all clean. The gripper view exists because a grasp asserted from a joint angle is not a grasp: it has to be seen closing on the object.
source: recordings/verification/06_full_autonomy/T1S2/... and .../T1/S1_both_arms_centre/rviz_gripper.mp4

## Slide 25
LANGUAGE
Understanding a free-form sentence
Wearable dual-arm supernumerary robot · shared autonomy
24
Zero MISUNDERSTOOD is the whole result
ASKED and REFUSED are both SAFE — the arm moved in neither. The bar is drawn at zero rather than omitted, so it reads as a measured zero and not an absence.
A wider parser sweep, 75 phrasings
34 correct / 14 asked / 27 refused / 0 misunderstood, against 21 / 14 / 37 / 3 for the grammar it replaced, run on the same cases in its own interpreter.
Ambiguity asks, and the ask is answerable
10 of the 14 asks carry a scored reply; all 10 resolve correctly, and a reply is never counted as CORRECT.
Voice is a PARSER score, never a transcription score. /dev/snd on this host has only 'timer', so no microphone can be opened and every voice figure came from synthesised audio.
source: recordings/baselines/language_vision_sweep.json (40 phrasings); scripts/sweep_t1_instructions.py (75)

## Slide 26
PART 4
Results
Grasping and placement, motion generation, the VR path, and the one measurement taken on real hardware.
25

## Slide 27
RESULTS
Headline results
Wearable dual-arm supernumerary robot · shared autonomy
26
100%
grasp success
17 cells × 8 angles, all five modes (2026-08-23 clip set)
0.000 mm
grasp positioning error
against a 30 mm capture gate
56.3 mm
T1 placement error
down from 319.7 mm before the re-record
12.91 mm
control budget, RSS
worst case 19.99 mm — inside the 30 mm gate for the first time
mode
task
n
grasped
positioning
placement
01 master
T3
2
2 / 2
0.00 mm
—
02 VR
T3
2
2 / 2
0.00 mm
—
03 shared
T3
2
2 / 2
0.00 mm
—
04 VR + shared
T3
2
2 / 2
0.00 mm
—
06 autonomy
T1
4
4 / 4
0.00 mm
55.5 – 56.9 mm
06 autonomy
T1S2
4
4 / 4
0.00 mm
—
T1 and T1S2 run under mode 06 only; T0 and the dance routines grasp nothing by design. Reading a by-design absence as a gap has been an instrument fault here three times.
source: recordings/verification/accuracy_table.json (2026-08-24)

## Slide 28
RESULTS
Grasp success and positioning error, per mode
Wearable dual-arm supernumerary robot · shared autonomy
27
grasp success, mode × task
positioning and placement error
Accuracy is TIED across all five modes on this clip set. That is the honest answer to 'is VR the most accurate mode': it is not distinguishable here, and this set PREDATES the 2026-08-26 VR smoothing.
source: recordings/verification/accuracy_table.json → recordings/analysis/ (2026-08-24)

## Slide 29
RESULTS
The same waypoints, different travel
Wearable dual-arm supernumerary robot · shared autonomy
28
The task layer commands identical waypoints under every mode — run_abc builds them with no mode argument. The robot does not perform identically: T0's left path is 1.407 m under mode 01 against 2.034 m under mode 03, measured with no operator present.
source: recordings/baselines/mode_difference.json (2026-08-15)

## Slide 30
RESULTS · MOTION
Motion generation: a per-joint clamp replaced by Ruckig
Wearable dual-arm supernumerary robot · shared autonomy
29
51.3 → 0.0
off-path excursion, mm
left arm; right 39.2 → 0.0, against a 30 mm gate
It never read joint_limits.yaml
17.5 rad/s commanded against a 1.3963 limit — 12.53×. Now 1.00×.
Not a tuning problem
swept against its own step size, the clamp's excursion SETTLES at 68 mm. It cannot be tuned into compliance.
Acceleration and jerk are ASSUMED and labelled
the yaml declares has_acceleration_limits: false for all fourteen joints. Velocity limits are the robot's.
motion_generator:=legacy reproduces any recording made before 2026-08-23.
source: recordings/baselines/teleop_motion.json (2026-08-23)

## Slide 31
RESULTS · VR
The VR path: smoothing, and where it stops working
Wearable dual-arm supernumerary robot · shared autonomy
30
stillness residual and reach lag
peak lag against peak hand speed
1-Euro against the EMA it replaced: 3.4× better stillness and 2.4× less lag. Under 0.27 m/s every protocol segment stays inside the 30 mm gate; the deliberate fast reach at 0.31–0.35 m/s does not. The smoothing figure is the filter maths recomputed through the shipped code — NOT a through-the-node or real-arm measurement.
source: srl_vr_teleop/vr_smoothing.py; recordings/vr_teleop/protocol_20260826_124739.json

## Slide 32
RESULTS · REAL HARDWARE
The simulation-to-hardware gap — measured on the real arms
Wearable dual-arm supernumerary robot · shared autonomy
31
0.305°
every joint parks short
on the side it came from; 211 of 252 errors in a 0.007° band
7.2 mm RMS at the end effector
on a 100 mm move, both arms.
A bound, not a spread
pushing the joint errors through the Jacobian reproduces the Cartesian error to 90%, r = 0.923 — a constant terminal offset.
ONE parameter per arm removes 74% / 76%
held out on an axis it was never fitted on, where a Cartesian 3×3 scores 93 mm.
36 real runs on the physical arms — the only hardware measurement in this deck. The COMPENSATION is modelled and has NOT been tried on hardware. The data already existed in arm_directional_calibration.json and nothing read it.
source: recordings/baselines/arm_directional_calibration.json, sim_to_real_gap.json (2026-08-23)

## Slide 33
RESULTS · INSTRUMENT
And the 'speed sweep' was not one
Wearable dual-arm supernumerary robot · shared autonomy
32
The claim
I reported the parking error as speed-independent across a 5× range.
What the data says
vmax_rad_s was read once at bridge start-up and never applied. 7 of 36 runs moved FASTER than the limit they were commanded with, and kortex_highlevel_bridge records this in its own source.
So
the three speeds are three REPLICATES of one condition. How the error varies with speed has NEVER been measured, and the file now says so in its own verdict field.
A control was added
which asserts the sweep still looks inert — so a genuine sweep makes the test fail and the stale sentences get rewritten.
This slide is a result. A measurement that contradicts an earlier one is an instrument check, not a finding, until the two are reconciled.
source: recordings/baselines/sim_to_real_gap.json → speed_sweep_was_inert; test_the_arm_stops_short_and_the_bridge_knows.py

## Slide 34
PART 5
Workspace characterisation
Why the arms barely move — sized in millimetres, per direction, per design choice, rather than asserted.
33

## Slide 35
WORKSPACE
Reachability, and two arms that cannot meet
Wearable dual-arm supernumerary robot · shared autonomy
34
reach per direction, both arms
the two reachable sets do not overlap
N = 10 repeats over the whole densified path, not one IK call — TRAC-IK restarts randomly and one call is one coin flip. The two arms' reachable sets are disjoint, which is why a handover task needs the right arm re-parked in hardware before it can exist at all.
source: recordings/baselines/workspace_n10_20260806.json

## Slide 36
WORKSPACE
What binds the workspace
Wearable dual-arm supernumerary robot · shared autonomy
35
direction
what limits it
measured
forward / outboard
the pinned wrist
0.065 m mean reach at the work point, against 0.450 free
inboard
the wearer — the TORSO, not their arms
min |x| 0.300 (L) / 0.375 (R) with the wearer's arms deleted entirely
down
the table
no configuration puts |x| ≤ 0.10 m on the surface; 3360 cells searched
top-down on a surface
not achievable at all
0 of 840 cells, any table height 0.70–1.10 m, either arm
any joint limit
nothing
no direction is bound by one
Folding the wearer's arms is worth 50 mm to the mannequin and NOTHING to a real person, because what binds changes identity: a limb for the mannequin, the torso every time for the person.
source: recordings/baselines/centre_vs_wearer_posture.json, centre_on_surface.json, wearer_size_effect.json

## Slide 37
WORKSPACE · SIZED
What the pinned wrist costs
Wearable dual-arm supernumerary robot · shared autonomy
36
0.065 m
pinned, at the work point
11 of 12 direction walks wearer-bound
0.325 m
with a 45° cone
the follower's own cone supplies it
0.450 m
fully free orientation
+385 mm, and only 4 walks wearer-bound
+0 mm
freeing the ROLL alone
refused by name — it buys nothing
The mechanism is not the wearer
A fixed 6-DOF pose on a 7-DOF arm spends the whole redundancy — and the redundancy is exactly the joint that moves the elbow out of the person while the hand stays put.
A factor of seven, and it was never sized before this measurement
From the HOME end-effector the penalty is only 89 mm; at the point where the work actually happens it is 385 mm. Measuring from the wrong start point is what hid it.
Nothing changes until a mode opts in
orientation_policy defaults to 'exact', so HARD CONSTRAINT 1 is untouched by the finding.
0.15 m wearer floor enforced under every policy, so the comparison is like for like.
source: scripts/measure_orientation_cost.py; docs/system/21_what_makes_the_workspace_small.md

## Slide 38
WORKSPACE
Mount geometry and the lateral constraint
Wearable dual-arm supernumerary robot · shared autonomy
37
mount position sweep
the lateral constraint
The mount was swept rather than chosen: 150 mm outboard and 15° of yaw is where the reachable set stops fighting the wearer. base_link still sits 161 mm from the torso and no joint moves it — so a clearance reading of exactly 0.1610 m is the MOUNT, not the arm.
source: recordings/baselines/gap_vs_mount.json, clearance_region.json

## Slide 39
WORKSPACE · BUDGET
The error budget, term by term
Wearable dual-arm supernumerary robot · shared autonomy
38
term
mm
systematic
note
terminal joint error, uncompensated
7.24
yes
0.305° per joint on 36 real runs
the same, overshoot switched on
1.88
yes
modelled, held out on an unseen axis — UNTRIED on hardware
shell bias, before the plane
10.50
yes
the object's bottom was unknown
the same, with the support plane
0.00
yes
the object RESTS on the plane, so its bottom is known
depth noise at 0.4–0.8 m
2.00
no
RealSense D4xx, subpixel-limited
IK solve residual
0.20
no
arm_ik reports its achieved residual; a refusal is searched
declared vs measured pad offset
0.05
yes
derived from the FK measurement since 2026-08-23
camera_link vs the physical module
UNMEASURED
yes
the largest remaining unknown — no CAD of the gripper here
RSS 18.64 → 12.91 mm, worst case 33.39 → 19.99 mm — inside the 30 mm capture gate for the first time. The pad row is COMPUTED from the constants, so reverting the derivation makes the budget say so.
source: recordings/baselines/control_budget.json; scripts/measure_control_budget.py

## Slide 40
PART 6
Method, limits and next steps
The operator's window, the instrument discipline that produced these numbers, and an honest account of what none of them support.
39

## Slide 41
OPERATOR
The window is the interface
Wearable dual-arm supernumerary robot · shared autonomy
40
Every capability reaches the window
A feature reachable only from a terminal does not exist for the person running the session.
257 checks, 0 failed
The audit presses every button AND checks what the press did — the e-stop must reach /estop, and a service button with no stack must say so.
A passing audit is not proof
Three defects lived for weeks behind a green return code: an invisible embedded RViz, a control column capped below its own content, and every mode button below the fold. So: launch it and look at it.
The audit's own worst catch: it had HUNG on a modal consent dialog since that dialog was added, so it never reached the presses that would have shown five buttons doing nothing silently inside a Qt slot.
source: recordings/session/20260824_190937/control_window.png; scripts/verify_gui_buttons.py

## Slide 42
OPERATOR
Commanded against actual, side by side
Wearable dual-arm supernumerary robot · shared autonomy
41
the embedded COMMANDED view
both panels and the divergence readout
RViz (COMMANDED) embedded beside a native ACTUAL panel drawn from the real_* frames, with the divergence readout under both. The RViz master draws three states, not two — commanded, actual, and PLANNED-BUT-REFUSED with its reason string, which cannot be drawn without one.
source: thesis_v2/figures/rviz_after_fix.png; docs/img/gui_dual_panels.png

## Slide 43
METHOD
The standing rule, and what it caught
Wearable dual-arm supernumerary robot · shared autonomy
42
Before reporting a bad measurement, validate the instrument.
A surprising failure is evidence about the INSTRUMENT until the instrument has been cleared. This has been the fault seventeen times.
what it looked like
what it actually was
T2's grippers never closed
run_abc held a grip until the pads REACHED the object — unsatisfiable for a task declaring grip_obj=None
A flaky autonomy task
clip_scene measured stage 2 at stage 1's approach: a 99.1 mm error in the MEASUREMENT, not the task
A grasp that was 13.47 mm short
PAD_MID_EE was derived, not measured — and the pad midpoint is a curve, not a constant: the fingers swing on a four-bar
A failing test called '='
the test gate matched ^FAILED over pytest output, and pep257 echoes the source lines it objects to
Three instruments reporting defects that did not exist
an i % 2 arm mapping, a by-design absence read as a gap, and a release demanded from a task that never releases
Every analysis script carries a known-answer test, and a check that cannot fail on a deliberately broken input is not a check.
source: CLAUDE.md — THE STANDING RULE; docs/system/findings.md

## Slide 44
LIMITS
What is verified, and what is not
Wearable dual-arm supernumerary robot · shared autonomy
43
MEASURED, AND THE FILE IS COMMITTED
— Grasping and placement across five modes, 17 cells × 8 angles
— The parking error, on 36 real-hardware runs
— Ruckig against the clamp it replaced, including the sweep showing the clamp cannot be tuned
— Workspace reach per direction at N = 10 over the whole path
— Clearance to the wearer, geometrically, per task
— Six injected perception faults, each refusal naming its own fault
— 1381 unit tests passing; 257 GUI checks, 0 failed
NOT MEASURED — AND NOT CLAIMED
— NO HUMAN DATA HAS BEEN COLLECTED AT ALL — blocked on ethics
— Speech recognition against a real speaker: /dev/snd has only 'timer', so every voice number came from synthesised audio
— The sim-to-real compensation, on hardware
— How the parking error varies with speed
— camera_link against the physical camera module — the largest remaining unknown in the budget
— Detection rate at working distance
— 7 of 14 master channels are incoherent; a soldering problem
Worn operation is >17 kg with no gravity compensation on someone who did not choose the motion. The operator and the wearer are different people and consent separately.
source: CLAUDE.md — Blocked on the lab / Blocked on ethics

## Slide 45
LIMITS
The study that is designed but not run
Wearable dual-arm supernumerary robot · shared autonomy
44
The protocol, the conditions and the analysis exist and are written up. No participant has been recruited: anonymity is enforced in code — write_manifest() raises on name, email, date of birth, address and phone — but consent has not been sought, so the participant results chapter is deliberately empty.
source: thesis_v2/figures/diagrams/experiment_design.tex; docs/research/

## Slide 46
CONCLUSION
Contributions
Wearable dual-arm supernumerary robot · shared autonomy
45
A working multimodal master interface
Four input routes — instrumented mannequin arm, VR controllers, shared autonomy over either, and a typed or spoken sentence — into one arm-command path, with the baseline condition kept free of in-repo dependencies so the comparison is not circular.
A safety architecture that measures the wearer rather than trusting the planner
The wearer's body and posture are variables with one source; the camera may only ever make that body BIGGER; and the clearance floor is enforced against the same body the planner sees.
A workspace characterisation that sizes its own constraints
The pinned wrist costs a factor of seven at the work point, the torso is what closes the centre, and top-down on a surface is not achievable at all — each with the search that establishes it.
Autonomy from a sentence, with zero misunderstandings
40 phrasings in the vision-coupled sweep and 75 in the parser sweep; ambiguity asks, and the ask is answerable in the same box.
An instrument discipline, and the ledger of what it caught
Seventeen occasions where the measuring tool was the fault, each written up with the mechanism — which is itself a result about how to evaluate a system like this.

## Slide 47
NEXT STEPS
Next, in order
Wearable dual-arm supernumerary robot · shared autonomy
46
#
what
why it is next
1
Off-axis directions in the calibration sweep
the 3×3 fit scores 93 mm held out on an axis — six axis-aligned directions are exactly a basis, with no redundancy to test
2
Try the terminal overshoot on hardware
modelled at 74% / 76% removal; both it and the 0.10° deadband are live parameters and four runs settle which wins
3
Measure camera_link against the physical module
the cheapest high-value calibration left, and the largest unknown in the budget
4
Attach a scene camera
the node, both calibration tools and their self-tests are built; no camera has ever been attached to this host
5
Repair the seven incoherent master channels
a soldering problem, with l_j2 and l_j4 named by regression
6
Ethics approval, then participants
the protocol is written; the arms are worn by one person and driven by another, and they consent separately
Ordered by what unblocks the most downstream work, not by effort.
source: docs/NEXT_SESSION_2026_08_23.md, docs/system/24_motion_planning.md

## Slide 48
Thank you
Everything shown is regenerated from committed recordings by scripts/make_presentation.py.
Evidence: recordings/verification/ (clips and the accuracy table) · recordings/baselines/ (every measurement) · recordings/analysis/ (the result figures) · docs/system/findings.md (the diagnostic history)